## Slide 1
Hans Wenzel
Krzysztof Genser
Soon Yung Jun
Fermilab
Integration of Opticks1 and Geant4
1developed by Simon Blyth

## Slide 2: CaTS:
Highly configurable (at runtime) Geant4 Application that allows to simulate Detector setups ranging from a single Detector (e.g. single crystal) to complex setups (e.g. test beam experiment consisting of many detector elements). It is used to demonstrate the G4Opticks hybrid workflow, works with Code: https://github.com/hanswenzel/CaTS. Use CaTS tag v_01_10_7_p01 when using geant4. 10.7.p01. The opticks commit point we are using is: commit c74e0670d232fe371eab056bc2c85fa33d33f69e (would be nice to have tags)
Features are:
Make use of Geant4 API, if something is missing add to Geant4 even if that means losing backward compability.
Uses gdml with extensions for flexible Detector construction and to provide optical properties at runtime. The gdml extensions include:
  Assigning sensitive detectors to logical Volumes. Available:
    RadiatorSD, lArTPCSD, TrackerSD, PhotonSD, TrackerSD, CalorimeterSD, DRCalorimeterSD,….
  Assigning step-limits to logical Volume
  Assigning visualization attributes.
Uses G4PhysListFactoryAlt to define and configure physics at runtime via command line option.
./G4OpticksTest -gdml G4Opticks_50000.gdml -pl 'FTFP_BERT+OPTICAL+STEPLIMIT+NEUTRONLIMIT’ -macro time.mac
Uses Root IO to provide persistency for Hits.
With G4opticks:
  Uses Geant4 to collect Scintillation and Cerenkov Gensteps. The Genstep harvesting is done in sensitive Detectors(SD) (RadiatorSD/lArTPCSD) the collection of the Photon Hits is done in PhotonSD.
  At runtime allows to select Opticks/Geant4 optical physics to generate and propagate optical photons, returns Photon-Hits.

## Slide 3: New CaTS workflow (with opticks)
TTree:
Event 1: lArTPCHits. PhotonHits. ……
Root file
Geant4 (Host)
G4Opticks(Device)
Generate and propagate Cerenkov and Scintillation photons
RadiatorSD::ProcessHits:
collect gensteps (C/S),
event loop:
Step:
End of event:
Begin of event:
gdml
.mac
input
output
Generate and propagate Cerenkov and Scintillation photons
g4ok->propagateOpticalPhotons
g4ok Hit
Gensteps (C/S)
Nr. Photons > NMAX:
Event 2: lArTPCHits. PhotonHits. ……
Event 3: lArTPCHits. PhotonHits. ……
PhotonHits
PhotonSD::AddOpticksHits
PhotonSD::AddOpticksHits
Gensteps (C/S)
PhotonHits
EventAction::EndOfEventAction
g4ok->propagateOpticalPhotons
g4ok Hit

## Slide 4: Plans
Short term:
  Continue working on 10.7.ref03/ref04  goal to be ready for Geant4.11.
  Make it an advanced Geant4 example.
  Integrate with the Fermilab liquid Argon experiments software stacks (LArSoft)  should be straightforward since the LArSoft Geant4 module is based on CaTS.
  Provide more realistic geometry examples
medium term:
  Update Opticks so it corresponds to the current Geant4 optical processes and uses the same properties.
  Implement wavelength shifting (WLS) process on GPU needed for LArTPCs.
  Enable Event based multithreading for the Geant4 process.
  Use G4Tasking (by J. Madsen) (available since Geant4 10.7).
  Keep up with Opticks development.